## Slide 1: Performance Tuning

## Slide 2: Hardware Tuning: Choice of RAID Level
To use RAID 1 or RAID 5?
  Depends on ratio of reads and writes
    RAID 5 requires 2 block reads and 2 block writes to write out one data block
If an application requires r reads and w writes per second
  RAID 1 requires r + 2w I/O operations per second (How?)
  RAID 5 requires: r + 4w I/O operations per second (How?)

## Slide 3: RAID Levels
RAID Level 1: Mirrored disks with block striping
Offers best write performance.
Popular for applications such as storing log files in a database system.
Example: You need 8TB of storage and there are available of 2TB disks.
How many disks will be needed for this storage system in RAID 1?
You have to store student relation file (B0, B1, B2, B3, B4, B5, B6, B7, B8, B9) into the storage system of RAID 1.
How?
B1
B5
B9
B2
B6
B3
B7
B0
B4
B8
D0 D1 D2 D3
RAID Level 1 (Mirroring)
D0 D1 D2 D3
DATA
D4 D5 D6 D7
MIRROR DISK
B1
B5
B9
B2
B6
B3
B7
B0
B4
B8
D4 D5 D6 D7
Question 35-1: If an application requires r reads and w writes per second, RAID 1 requires r + 2w I/O operations per second (How?)

## Slide 4: RAID Levels (Cont.)
RAID Level 5: Block-Interleaved Distributed Parity;
partitions data and parity among all N + 1 disks.
E.g., with 5 disks, parity block Pk for blocks 4k, 4k+1, 4k+2, 4k+3 is stored in disk k mod 5.
For k=0, blocks B0, B1, B2, B3, parity block P0 is stored in disk (0 mod 5 = 0) D0 disk.
For k=1, blocks B4, B5, B6, B7, parity block P1 is stored in disk (1 mod 5 = 1) D1 disk.
Example: You need 8TB of storage and there are available of 2TB disks.
How many disks will be needed for this storage system in RAID 5?
RAID Level 5 (Block striping distributed parity)
B0
P1
B9
B1
B5
B2
B6
P0
B4
B8
D0 D1 D2 D3 D4
B3
B7

## Slide 5: RAID Levels (Cont.)
Parity blocks: Parity block stores XOR of bits from corresponding blocks of each disk
How is recovery performed single disk failure?
To recover data for a block, compute XOR of bits from all other blocks in the set including the parity block
What will happen if two disks failed simultaneously?
How is update block B3 performed?
READ B3, P0 into memory
Update B3 to B‘3 and compute P‘0 using B3 and B‘3
WRITE B‘3 , P‘0 to disk.
Example: You need 8TB of storage and there are available of 2TB disks.
How many disks will be needed for this storage system in RAID 5?
RAID Level 5 (Block striping distributed parity)
B0
P1
B9
B1
B5
B2
B6
P0
B4
B8
D0 D1 D2 D3 D4
B3
B7
Question 35-2:
If an application requires r reads and w writes per second, RAID 5 requires: r + 4w I/O operations per second (How?)

## Slide 6: RAID Levels (Cont.)
RAID Level 5 (Block striping distributed parity)
Example: You have been given six disks of 2TB each.
What are the effective storage capacity in RAID 1, RAID 5?
Effective storage capacity in RAID 1 = 6TB
Effective storage capacity in RAID 5 = 10TB
b. Show the storage of blocks B0, B1, B2, B3, B4, B5, B6, B7, B8, B9 into 6 disks using RAID5.
B0
P1
B1
B6
B2
B7
P0
B5
D0 D1 D2 D3 D4 D5
B3
B8
B4
B9

## Slide 7: Hardware Tuning: Choice of RAID Level
For reasonably large r and w, this requires lots of disks to handle workload
  RAID 5 may require more disks than RAID 1 to handle load!
  Apparent saving of number of disks by RAID 5 (by using parity, as opposed to the mirroring done by RAID 1) may be illusory!
Thumb rule: RAID 5 is fine when writes are rare and data is very large, but RAID 1 is preferable otherwise
  If you need more disks to handle I/O load, just mirror them since disk capacities these days are enormous!